## Slide 1
Akhil Gharpurey
Undergraduate Research Assistant – Bakolas Research Group
Department of Aerospace Engineering and Engineering Mechanics, The University of Texas at Austin
APRIL 2026
Terrain-aware model-predictive path integral control
M E 177K Final Deliverable

## Slide 2: Contents
Overview
Model-Predictive Path Integral Control
Dynamic Obstacle Handling
Terrain Perception and Evaluation
Simulation and Results
2

## Slide 3
Introduction
Introduction to Autonomous Navigation and Path Planning

## Slide 4: Overview
Aim to solve the autonomous navigation problem
  Goal: reach a desired position from a given start position while minimizing some performance index
Problem extends to various applications, such as package delivery and planetary navigation
4

## Slide 5: Existing Solutions (1)
Path Planning Algorithms [1]
  A*: Finds optimal path from start to end goal via heuristics
  Does not do any local online motion planning
5
Figure 1: A* Path Planning Implementation

## Slide 6: Existing Solutions (2)
Reinforcement Learning [1]
  Iteratively learns the correct path to take
  Difficult to deploy in real-time scenarios
6
Figure 2: RL Path Implementation

## Slide 7: Enabling Online Motion Planning
Aim: Derive a trajectory and track it in real time while approaching goal position
Need real-time control algorithm which can perform this task
7

## Slide 8: Model-Predictive Control (MPC)
MPC optimizes a control sequence generated over a finite time horizon
Generates local trajectory and computes the optimal control input to apply to the system dynamics
8
Figure 3: MPC Implementation in Autonomous Racing

## Slide 9: MPC - Mathematical Formulation
9
For linear systems, this reduces to an iterative QP problem [2]

## Slide 10: Stochastic MPC and MPPI (1/2)
10
Baseline MPC assumes perfect knowledge of state and control input
  No ability to handle noise
Stochastic MPC (SMPC) methods are necessary for noise/disturbance rejection

## Slide 11: Stochastic MPC and MPPI (2/2)
11
First and second order methods are often employed to solve SMPC problems
  May converge to local minima not equal to the true minimum [3]
Zero order sampling-based methods are often used to alleviate this

## Slide 12
MPPI Control
What is MPPI?
MPPI Control Problem Formulation
MPPI Solution Algorithm
Deployment in Static Environments

## Slide 13: Introduction to MPPI
13
Zero-order algorithm for solving SMPC problems
Samples several input perturbations in parallel and optimizes the set of trajectories instead of iterating on one sequence

## Slide 14: General SMPC Problem Formulation
14

## Slide 15: MPPI Solution Algorithm (1/2)
15
First generates M (≈ 103−104) input sequence perturbations around a nominal control sequence
  Samples from Mixture-of-Gaussians (MoG) with zero mean and covariance
  Nominal control sequence is initialized at zero
Computes cost for each perturbed control sequence according to cost functional J(x,u) where x is the trajectory generated by the control sequence u

## Slide 16: MPPI Solution Algorithm (2/2)
16
Weights each control sequence according to cost relative to minimum
Optimal Control Input is computed as weighted sum of perturbations

## Slide 17: MPPI with Static Obstacle Handling
17
Apply additional constraint to optimization problem
  Denote Xk,rbt as the space comprised of the robot geometry, Xobs as the space comprised of all obstacles in the given environment
Becomes a soft constraint with large penalty in simulation

## Slide 18: Baseline MPPI – Deployment (1/4)
18
Deployed on a kinematic differential drive model with dynamics
  State Vector: xk = [x y θ]k
  Control Input Vector: uk=[vl vr]k

## Slide 19: Baseline MPPI – Deployment (2/4)
19
Generated 20,000 samples with 40 time horizon steps
Environment is a corridor with width 8.0 m and length 28.0 m
  10 static circular obstacles are randomly placed throughout the environment
Initial position: (0.0, 0.0); Goal position: (0.0, 20.0)

## Slide 20: Baseline MPPI – Deployment (3/4)
20
Cost evaluation of samples is parallelized on a CUDA kernel
Ran on 16-core 13th Generation Intel i7-1360P and NVIDIA RTX 3050 GPU with 4GB VRAM and 32GB RAM
Achieved computation time of 5 ms per step (200 Hz control frequency)
Figure 4: Baseline MPPI Implementation

## Slide 21: Baseline MPPI – Deployment (4/4)
21
Observed some undesired behavior; ex. backwards motion (left), entrapment (right)
Figure 5: Baseline MPPI Simulation exhibiting Backwards Motion
Figure 6: Baseline MPPI Simulation exhibiting Entrapment

## Slide 22
Robust Mppi in dynamic environments
Avoiding Entrapment through Real-Time Covariance Adaptation
Dynamic Obstacle Handling

## Slide 23: Entrapment Problem
Robot experiences a “trap” where it is surrounded by obstacles
  Unable to derive a solution which continues navigation towards goal
Mathematical Definition:
23
Figure 7: Entrapped robot

## Slide 24: Solution to Entrapment
Aim to increase the probability of generating an escape trajectory
  Solution A (trivial): Increase M
  Solution B: Increase perturbation covariance Σ when close to obstacles
Increasing the number of samples increases computational load so we opt for solution B
24

## Slide 25: Covariance Adaptation (1/2)
Manipulating covariance based on presence of obstacles yields higher escape probability
  Proof Linked Here
Discriminate generated trajectories as “safe” or “unsafe”
  Safe: away from obstacles all time steps
  Unsafe: near an obstacle at some time step
25

## Slide 26: Covariance Adaptation (2/2)
For each rollout, derive the danger D
26
Update covariance based on observed danger with a maximum threshold μmax

## Slide 27: Dynamic Obstacle Modeling (1/2)
27
Model dynamic obstacles after low-fidelity humanistic motion
Assumptions: constant speed, direction changing follows first-order steering dynamics

## Slide 28: Dynamic Obstacle Modeling (2/2)
28
Probabilistically changes direction with a probability α = 0.05
Incorporate inter-obstacle collision avoidance
  Set desired velocity based on repulsion
Figure 8: Repulsion between Neighboring Obstacles

## Slide 29: Dynamic Obstacle Handling
29
Utilize Monte Carlo rollout sampling to generate R predicted obstacle trajectories over the same time horizon (R ∈ [40, 50])
  Evaluate costs across all obstacle rollouts for each robot trajectory
  Obstacle trajectory prediction takes current position and velocity as inputs
R is kept small to prevent large computational overhead while maintaining robust prediction capabilities

## Slide 30: Simulation of Dynamic MPPI (1/2)
30
Deploy in square environment with start position (0,0) and goal position (10,10) to allow obstacles room to traverse
Create 7 obstacles with a speed of 1.34 m/s (human walking pace) and randomized initial positions and headings
Obstacles have robot avoidance strategy by treating robot as neighboring obstacle
Figure 9: Robust Dynamic MPPI Implementation in Superflat Terrain

## Slide 31: Simulation of Dynamic MPPI (2/2)
31
Step solve time of 0.028 seconds for 7 obstacles, 50 rollouts, and 15000 samples => control frequency of 36 Hz
Average collision probability = 0.10
  Taken by computing complement of proportion of safe trajectories
Figure 10: Velocity, Covariance, and Orientation over Time

## Slide 32
Terrain awareness in mppi control
Quantitative Terrain Evaluation via Digital Elevation Map Rendering
Qualitative Terrain Evaluation via Bayesian Classification
Robust Navigation via Waypoint Heuristics

## Slide 33: Quantitative Terrain Evaluation (1/4)
33
In terraneous environments, robots may be prone to slip or excess battery/fuel consumption
Need a method for optimizing path across terrain
  Goal: Acquire understanding of local terrain and determine terrain cost

## Slide 34: Quantitative Terrain Evaluation (2/4)
34
How do we acquire terrain knowledge?
  Simulate visual sensor (camera)
  Extract square images with a specified horizontal FOV angle and vertical FOV
  Performs parallelized ray marching algorithm to find all intersections with terrain
  Generates local point of view of terrain with noisy elevation and slope estimates
Figure 11: Camera sensor optics (generated by Claude Opus 4.6)

## Slide 35: Quantitative Terrain Evaluation (3/4)
35
Derive digital elevation map (DEM) from camera point cloud
  Camera point cloud → continuous patches “stitched” together
  Slope and roughness are computed for each patch
For patches repeatedly observed, the DEM fuses each observation and increases confidence and precision for each patch estimate

## Slide 36: Quantitative Terrain Evaluation (4/4)
36
Using DEM estimates, acquire a costmap of the terrain
Figure 12: Rendered Digital Elevation Map vs. Ground Truth
Figure 13: Observed Costmap, Confidence, and Error

## Slide 37: Qualitative Terrain Evaluation (1/3)
37
Quantitative (DEM) approach only provides soft constraint – could be insufficient for fully preventing robot tip-over
Goal: mask out dangerous terrain such that the robot navigates on traversable terrain exclusively
  Approach: Bayesian classification of terrain patches

## Slide 38: Qualitative Terrain Evaluation (2/3)
38
Define 8-dimensional feature vector of each patch
Using Bayes’ Theorem, determine probability of belonging to each class
Ci = class, P(Ci|v) = posterior probability, P(v|Ci) = likelihood, P(Ci) = prior, P(v) = evidence

## Slide 39: Qualitative Terrain Evaluation (3/3)
39
Obtain class priors by bootstrapping the algorithm
  Classifier uses a circular buffer to store simulated results for all cells in given terrain
    Class means, variances, and priors are obtained
    Bootstrapped results eventually get diluted by posterior estimates from online learning
  Each cell is classified as traversable (zero cost multiplier), cautious (half cost multiplier), and non-traversable (full cost)
Costs of each cell class are added to terrain costmap

## Slide 40: Waypoint-Heuristic Motion Planning (1/4)
40
Quantitative and qualitative terrain costmap introduces local minima located away from goal position
  Covariance adaptation insufficient for driving robot away from terrain-driven minima
  Need robust method of driving robot towards goal incrementally, discouraging settling at local minima
Proposed solution: create a waypoint heuristic which selects subgoals along the robot’s way towards the goal

## Slide 41: Waypoint-Heuristic Motion Planning (2/4)
41
Setup: lay out local grid with robot at center with 2k+1 nodes in each row and column
Heuristic is weighted sum of progression towards goal (π), terrain costmap (Qtr), and obstacle aversion

## Slide 42: Waypoint-Heuristic Motion Planning (3/4)
42
Path-integral procedure is applied for deriving optimal waypoint coordinates
The optimal waypoint is treated as goal position until robot reaches it
  Forces waypoint recalculation

## Slide 43: Waypoint-Heuristic Motion Planning (4/4)
43
Weights determine priority of constraint
  For large βp, we prioritize progress towards the goal
  For large βo, we heavily prioritize obstacle avoidance
    May observe subgoal recalculation if intercepted by obstacle
  For large βt, we prioritize traversing safe terrain
Figure 14: Waypoint Heuristic Diagram with Minimizer (red) and Optimal Waypoint (blue)

## Slide 44
Simulations and results
Algorithm Demonstration
Computational Evaluation
Future Work

## Slide 45: Algorithm Block Diagram
45
Bootstrap Bayes Classifier
Sense Terrain with Camera
Classify Terrain Traversability
Create/Render Digital Elevation Map
Build costmap, port to cost function
MPPI Control
Obstacle Motion
Robot Dynamics
Figure 15: Fully Integrated Algorithm Block Diagram

## Slide 46: Simulation Example (1/5)
46
Figure 16: Bird’s Eye View of Hilly Terrain Simulation
Figure 17: Camera POV of Hilly Terrain Simulation

## Slide 47: Simulation Example (2/5)
47
Figure 18: Hilly Terrain Observed Costmap with Confidence and Error Shown (online learning time per step = 4.9 ms)
Figure 19: Rendered Digital Elevation Map

## Slide 48: Simulation Example (3/5)
48
Figure 20: Bird’s Eye View of Rough Terrain Simulation
Figure 21: Camera POV of Rough Terrain Simulation

## Slide 49: Simulation Example (4/5)
49
Figure 22: Rough Terrain Observed Costmap with Confidence and Error Shown (online learning time per step = 4.9 ms)
Figure 23: Rendered Digital Elevation Map

## Slide 50: Simulation Example (5/5)
50
Figure 24: Covariance, Velocity, and Orientation over Time in Hilly Terrain
Figure 25: Covariance, Velocity, and Orientation over Time in Rough Terrain

## Slide 51: Results
51
Simulations were conducted with 15,000 samples, 40-step time horizon at Δt = 0.05 s, and 8 obstacles (7 dynamic, 1 static)
  Achieved MPPI solve step time of 30.6 ms and online learning of 5-6 ms (rougher terrain → more cells to learn)
  Total control loop frequency = 27.7 Hz
    Exceeds real-time threshold frequency of 20 Hz
  Over 100 simulations, zero failures occurred via obstacle collision
    Average safe trajectory rate = 0.877 → collision probability = 0.123
    Maximum robot pitch = 19.8o, Maximum robot roll = 14.2o

## Slide 52: Future Work
52
Eliminate omniscience in obstacle detection
  Implement a method of observing dynamic obstacles on camera
  Adjust computation time depending on number of observed static and dynamic obstacles
Develop and implement robust safety measures to guarantee safe navigation [5]
Accelerate obstacle computation to guarantee real-time performance [6]

## Slide 53
Thank you!

## Slide 54: References (1/2)
54
[1] Sangeeth Venu, Muralimohan Gurusamy, A comprehensive review of path planning algorithms for autonomous navigation, Results in Engineering, Volume 28, 2025, 107750, ISSN 2590-1230, https://doi.org/10.1016/j.rineng.2025.107750.
[2] A. Bemporad, M. Morari, V. Dua and E. N. Pistikopoulos, "The explicit solution of model predictive control via multiparametric quadratic programming," Proceedings of the 2000 American Control Conference. ACC (IEEE Cat. No.00CH36334), Chicago, IL, USA, 2000, pp. 872-876 vol.2, doi: 10.1109/ACC.2000.876624.
[3] Homburger, H., et al. "Optimality and Suboptimality of MPPI Control in Stochastic and Deterministic Settings," in IEEE Control Systems Letters, vol. 9, pp. 763–768, 2025.

## Slide 55: References (2/2)
55
[4] R. Lacroix, "Autonomous Rover Navigation on Unknown Terrains Functions and Integration," in Experimental Robotics VII, 2001, pp. 501–510.
[5] Pedram Rabiee, Jesse B. Hoagg, "Guaranteed-Safe MPPI Through Composite Control Barrier Functions for Efficient Sampling in Multi-Constrained Robotic Systems," 2024.
[6] Steven Patrick, Efstathios Bakolas, "Path Integral Control with Rollout Clustering and Dynamic Obstacles," 2024.